## Slide 1
Computer Systems
For AI-inspired Cloud
Theory & Lab.
https://github.com/SmartX-Labs/SmartX-Mini-MOOC
Lab #2: Inter-Connect

## Slide 2
Hypriot OS
Ubuntu Linux
Raspberry Pi
NUC
Kafka broker cluster
Inter-Connect Lab: Concept

## Slide 3
Physical Inter-Connect
Docker
Runtime
C
Hypriot OS
Switch
Raspberry Pi Box
for IoT Sensors
& Actuators
NUC Box
for IoT-Cloud Hub
Linux Ubuntu OS
KVM Hypervisor
iperf Server
iperf Client
iperf Client
VM
Container
TCP Packet

## Slide 4
……
Topic 2
(Memory Utilization)
Topic 3
(CPU Utilization)
Topic 4
(IO)
Topic 1 (Load Average)
Timestamp, IP Address, Value1
Timestamp, IP Address, Value1
….
Timestamp, IP Address, Value1, Value2, …
Timestamp, IP Address, Value1, Value2, …
Timestamp, IP Address, Value1, Value2, …
…
Kafka Cluster
Data Inter-Connect

## Slide 5
Theory

## Slide 6: Computer System: Inter-Connected Functions inside/across Boxes/Sites
Functions
Inter-Connect
Resources – Workloads - Services
Box
Site

## Slide 7
Inter-Connect Test: iperf
http://sfixer.tistory.com/entry/iperf-The-Easy-Tutorial
Simply measures the maximum transmission capacity (bandwidth) in the wired / wireless network communication section
Transmits the maximum traffic from Client node to the Server node and displays the result.
Support TCP, UDP, SCTP and so on.
Support variety of options
  -s : iperf server
  -c : iperf client
  -i : check interval time
  -t : total check time

## Slide 8
Kafka Messaging System
Kafka Cluster
broker1
Zookeeper
Cluster
Producer
Consumer
Broker2
(Leader)
broker3
TCP Protocol
TCP Protocol
Topics: maintains feeds of messages in categories
Producers: processes that publish messages to a Kafka topic
Consumers: processes that subscribe to topics and process the feed of published messages
Broker: run as a cluster comprised of one or more servers
Provides the functionality of a messaging system, but with a unique design
Zookeeper
Producers(Pi #1)
Node 0 (Master)
Broker 0
Node 1 (Slave 1)
Broker 1
Node 2 (Slave 2)
Broker 2
Consumers
(Spark Streaming)
Producers(Pi #2)
Producers(Pi #20)
Node 3 (Slave 3)
Broker 3
. . . . . . . .

## Slide 9
Net-SNMP: SNMP Agent/Manager
(Simple Network Management Protocol): Used in network management systems to monitor network-attached devices, which include routers, switches, servers, workstations, printers, modem racks and more
  Manager : polls agents on the network, correlates and displays information
  Agent : collects and stores information, responds to manager requests for information, generates traps
A suite of software for using and deploying the SNMP Protocol

## Slide 10
Apache Flume: Log Collector
A distributed, reliable, and available service for efficiently collecting, aggregating, and moving large amounts of log data
Log aggregator with many customizable data sources, which runs asynchronously
Flume Agent
  Source consumes events having a specific format
  Channel holds the event until consumed
  Sink removes an event from the channel and puts it into on external repository or another source

## Slide 11: Docker: Light-weight Process (Application) Container
Docker Hub

## Slide 12
Practice

## Slide 13: NAME: NUC5i5MYHE (NUC PC) CPU: i5-5300U @2.30GHz CORE: 4 Memory: 16GB DDR3 HDD: 94GB
Wired connection
NAME: Raspberry Pi Model B (Pi) CPU: ARM Cortex A7 @900MHz CORE: 4 Memory: 1GB SD Card: 32GB
NAME: netgear prosafe 16 port gigabit switch(Switch) Network Ports: 16 auto-sensing 10/100/1000 Mbps Ethernet ports
NAME: NT900X3A
CPU: i5-2537U @1.40GHz
CORE: 2 Memory: 4GB DDR3 HDD: 128GB
#0 Lab Preparation (1/3)

## Slide 14
#0 Lab Preparation (2/3)
-Verify Box Lab’s configuration
eth0
br0
VM
Container
Tap1
ping test
$ ping <VM IP>
$ ping <Container IP>

## Slide 15
#0 Lab Preparation (3/3)
Prepare 3 terminal on NUC
  Bare metal, VM, Container
Running and Access to KVM on NUC (Open KVM terminal)
  $ sudo kvm -m [memory capacity] -name [name] -smp cpus=[#cpu],maxcpus= [#maxcpu] -device virtio-net-pci,netdev=net0,mac= [EE:EE:EE:EE:EE:EE] –netdev tap,id=net0,ifname= [tap_name],script=no -boot d [name].img -vnc :[#] -daemonize
  $ xvnc4viewer localhost :5
Access to Container on NUC (Open Container terminal)
  $ docker attach [container name]

## Slide 16
#1–1 Raspberry PI: OS Installation (1/3)
Before we start, your Raspberry Pi must be ready with proper OS.
In this lab, we will use “HypriotOS” Linux for it.
Eject a MicroSD card from your Raspberry Pi, and insert it into your SD card reader and attach the reader to your NUC.
Issue the commands below to get “flash” script for the OS setup.
Issue “flash” command to see if it’s installed correctly.
  $ sudo apt update && sudo apt install -y pv curl python-pip unzip hdparm
  $ sudo pip install awscli
  $ curl -O https://raw.githubusercontent.com/hypriot/flash/master/flash
  $ chmod +x flash
  $ sudo mv flash /usr/local/bin/flash

## Slide 17
Download & edit HypriotOS configuration file for your Raspberry Pi.
  $ wget -O hypriot-init.yaml https://mirror.nm.gist.ac.kr/getHypriotConf
  Let’s open the “hypriot-init.yaml” file and edit its network section.
The assigned IP address will be automatically applied, when you’re initially booting your Raspberry Pi.
$ sudo vi hypriot-init.yaml
…
# static IP configuration:
interface eth0
static ip_address=172.29.0.250/24 # Write your Raspberry Pi address
static routers=172.29.0.254
static domain_name_servers=8.8.8.8 8.8.4.4
…
#1–2 Raspberry PI: OS Installation (2/3)

## Slide 18
#1–2 Raspberry PI: OS Installation (3/3)
  $ sudo fdisk –l
  $ flash –u hypriot-init.yaml –d /dev/sdc –f https://mirror.nm.gist.ac.kr/getHypriot
And, that’s it! Now HypriotOS is flashed to your MicroSD card.
Insert the SD card back to your Raspberry PI and boot it up.

## Slide 19
Physical Inter-Connect test
Docker
Runtime
C
Hypriot OS
Switch
Raspberry Pi Box
for IoT Sensors
& Actuators
NUC Box
for IoT-Cloud Hub
Linux Ubuntu OS
KVM Hypervisor
iperf Server
iperf Client
iperf Client
VM
Container
TCP Packet

## Slide 20
#2 Network Configuration:
Check Network & install packages
Check network interface configuration
  $ ifconfig
Check routing table and install packages
  $ netstat –rn
  $ sudo apt-get install openssh-server git vim

## Slide 21
iperf server install on Raspberry PI
  $ sudo apt-get install iperf
iperf client install on NUC baremetal
  $ sudo apt-get install iperf
iperf client install on NUC KVM
  $ sudo apt-get install iperf
iperf client install on NUC Container
  $ sudo apt-get install iperf
#3-1 iperf test: installation

## Slide 22
#3–2 iperf test: Execute iperf
Execute iperf Server on Raspberry PI
  $ iperf –s
  Iperf server must execute before you execute client
Execute iperf client on NUC baremetal, VM, and Container
  $ iperf –c <Raspberry PI IP address> -i 1 –t 30
  (Do not execute at the same time)
<iperf result (baremetal)>
<iperf result (VM)>
<iperf result (Container)>

## Slide 23
#3–3 iperf test: Check Result
<iperf result (baremetal)>
<iperf result (VM)>
<iperf result (Container)>
<iperf Server result>
Baremetal Result
VM Result
Container Result

## Slide 24
Every machine which communicate with themselves must know their own address.
Edit /etc/hosts
(For Example)
Add two lines which describe the IP address and hostname of devices
IP address
hostname
  $ sudo vi /etc/hosts
#4–1 Hostname preparation for Kafka (1/2)

## Slide 25
Every machine which communicate with themselves must know their own address.
SSH access to your PI (ID: pirate, PW: hypriot)
  $ ssh pirate@<your Raspberry PI IP Address>
Edit /etc/hosts
  $ sudo vi /etc/hosts
(For Example)
Add two lines which describe the IP address and hostname of devices
#4–1 Hostname preparation for Kafka (2/2)

## Slide 26
#4–2 Verification for hostname preparation
After editing /etc/hosts, check the edit is correctly done
For NUC
  $ ping <Your NUC hostname>
  $ ping <Your Raspberry PI hostname>
For Raspberry PI
  $ ping <Your NUC hostname>
  $ ping <Your Raspberry PI hostname>
If it was successful, We can be sure that
NUC know its own hostname and Pi’s hostname and Pi also know its own hostname and NUC’s hostname.

## Slide 27
Hypriot OS
You
Raspberry Pi
NUC
Kafka broker cluster
Ubuntu Linux
Data inter-connect with Kafka: NUC-side configuration

## Slide 28
#5–1 Kafka deployment: Docker file download
In this section, we use this
Download all files from Github
(http://github.com/SmartXBox/SmartX-mini)
  $ git clone https://github.com/SmartXBox/SmartX-mini.git
Folder List

## Slide 29
#5–1 Download Files from Github
- Allocate Broker IDs and Ports
We’ll use a one zookeeper, 3 brokers and one consumer containers which share host’s public IP address
Zookeeper container doesn’t have broker id.
Each Broker has a unique id and port to interact each other.
Consumer container just used to manage topic and check the data from brokers.
Function(Container) Name | IP address | Broker id | Listening port
Zookeeper | Host’s public IP address | - | 2181
Kafka broker0 |  | 0 | 9090
Kafka broker1 |  | 1 | 9091
Kafka broker2 |  | 2 | 9092
Kafka consumer |  | - | -

## Slide 30
#5–2 Kafka deployment: Build Docker Image
Build Docker Image
  $ cd ~/SmartX-mini/ubuntu-kafka
Build Dockerfile ※ It takes long time. You should type ‘.’ !
  $ docker build --tag ubuntu-kafka .
If you want to check Docker instruction words
  $ docker --help
  ex) docker ps : List containers
  docker start : Start one or more stopped containers
  docker rm : Remove one or more containers

## Slide 31
#5–3 Kafka deployment: Place Docker Containers
(Recommend open new terminal window)
Run Docker Container
  $ docker run -it --net=host --name [container name] ubuntu-kafka
  We need to run 5 containers (zookeeper 1, broker 3, consumer 1)
  Let’s assume the name of each containers,
    zookeeper, broker0, broker1, broker2, consumer
  Repeatedly type the above command with changing container name
  If you want to look for more details about Docker command, see https://docs.docker.com/reference/commandline/

## Slide 32
-Zookeeper properties
#6–1 Kafka Containers: Zookeeper configuration
Actually we use default configuration
Open zookeeper properties file
  $ vi config/zookeeper.properties
Check the client port

## Slide 33
zookeeper must execute first
  $ bin/zookeeper-server-start.sh config/zookeeper.properties
  (Leave Zookeeper running and open a new terminal for next tasks)
#6–2 Kafka Containers: Zookeeper executing

## Slide 34
#6–3 Kafka Containers: Kafka Broker configuration
Create a Kafka container with the docker command before
  $ docker run -it --net=host --name [container name] ubuntu-kafka
Open server properties file and change proper broker id and port (they must be unique to each other) (Only for broker0,1,2)
  $ vi config/server.properties
broker id
port
Container Name | Broker id | Listening port
broker0 | 0 | 9090
broker1 | 1 | 9091
broker2 | 2 | 9092
consumer | - | -
Consumer container will not run any brokers

## Slide 35
Execute Kafka brokers (Only for broker0,1,2)
  $ bin/kafka-server-start.sh config/server.properties
Repeat previous steps for broker0, broker1, broker2,consumer
When it successfully works, each broker containers will show messages like the below
#6–4 Kafka Containers: Kafka Broker executing

## Slide 36
#6–5 Kafka Containers: Make Topic
Create topic
  $ bin/kafka-topics.sh --create --zookeeper localhost:2181 --replication-factor 1 --partitions 3 --topic resource
We can check topics.
Topic List
  $ bin/kafka-topics.sh --list --zookeeper localhost:2181
Topic specification
  $ bin/kafka-topics.sh --describe --zookeeper localhost:2181 --topic resource
resource

## Slide 37
Hypriot OS
Ubuntu Linux
You
Raspberry Pi
NUC
Kafka broker cluster
Hypriot OS
Data inter-connect with Kafka: PI-side configuration

## Slide 38
Git package is already installed in Hypriot OS
Download all files from Github
(http://github.com/SmartXBox/SmartX-mini)
  $ git clone https://github.com/SmartXBox/SmartX-mini.git
Folder List
In this section, we use this file
#7–1 Flume on Raspberry PI: File download

## Slide 39
Update packages
  $ sudo apt update
Download Net-SNMP
  $ sudo apt install –y snmp snmpd snmp-mibs-downloader
Download MIBs
  $ sudo download-mibs
Modify configuration file
  $ sudo vi /etc/snmp/snmpd.conf
    #rocommunity public localhost -> Delete #
  $ sudo systemctl restart snmpd.service
#7–2 Flume on Raspberry PI: Net-SNMP installation

## Slide 40
Build Dockerfile ※ It takes long time. You should type ‘.’!
  $ cd SmartX-mini/raspbian-flume
  $ vi Dockerfile
  modify wheezy  wheezy-20180926
  $ docker build --tag raspbian-flume .
  $ docker run -it --net=host --name flume raspbian-flume
Check the configuration file
  $ vi conf/flume-conf.properties
Modifying broker list
  Default value sets “nuc”
  Edit them into your own nuc’s hostname
#7–3 Flume on Raspberry PI: Flume installation

## Slide 41
Run Flume on RPi
  $ bin/flume-ng agent --conf conf --conf-file conf/flume-conf.properties --name agent -Dflume.root.logger=INFO,console
#7–4 Flume on Raspberry PI: Executing Flume agent

## Slide 42
Hypriot OS
Ubuntu Linux
You
Raspberry Pi
NUC
Hypriot OS
Data inter-connect with Kafka: Verification
Kafka broker cluster

## Slide 43
#8 Consume message from brokers
Launch consumer script on the Consumer container
  $ bin/kafka-console-consumer.sh --zookeeper localhost:2181 --topic resource --from-beginning

## Slide 44
Review

## Slide 45
With Inter-Connect Lab, you have experimented
  How to physically inter-connect two kinds of Boxes (NUC and Raspberry PI)
  How to inter-connect data transfer (via Kafka messaging) between functions located in different boxes
  Differentiation between two types of “Inter-connect”: You need to distinguish physical Inter-connect from data Inter-connect!
Lab Summary

## Slide 46
Thank You for Your Attention
Any Questions?
mini@smartx.kr